## Slide 1: VSS-core analysis
Ulf Björkengren Ford Motor Company
February 24 2025

## Slide 2: Analysis of transforming VSS to VSS-core
VSS tree nodes (250211):Vehicle.*: 1815
  Vehicle.ADAS.*: 90
  Vehicle.Body.*: 126
  Vehicle.Cabin.*: 763
  Vehicle.Chassis.*: 88
  Vehicle.CurrentLocation.*: 13
  Vehicle.Driver.*: 10
  Vehicle.MotionManagement.*: 96
  Vehicle.OBD.*: 143
  Vehicle.Occupant.*: 87
  Vehicle.Powertrain.*: 222
  Vehicle.VehicleIdentification.*: 22
  Vehicle.VersionVSS.*: 5
  Vehicle.xxx: 1815-1665= 150
Analysis
  Entire branches that may be removed (~240 nodes):
    OBD
    Driver
    Occupant
  Cabin is mainly Seat, which have vehicle specific layouts.
  Chassis is mainly Axle/Wheel, which have vehicle specific layouts.
  Significant parts of this tree will have to be represented in the vehicle specific tree if Cabin and Chassis are moved out of the VSS-core tree.

## Slide 3: How to represent vehicle specific instantiations in VSS-core
The argument for having a vehicle type agnostic data representation is that an app developed for one vehicle type (e.g. Pass cars) should also work for other vehicle types (e.g. Trucks).
With a small effort placed on the app developer it is possible to include vehicle specific instantiations in the representation, thus making it possible to include e.g. Seat and Axle/Wheel.
Example paths:
  Passcar: "Vehicle.Chassis.Axle.Row1.Wheel.Left.Brake.FluidLevel"
  Truck: "Vehicle.Chassis.Axle.Row1.Wheel.Pos6.Brake.FluidLevel”
If the app is provided with info about the instantiation details it can easily adapt the path expressions.

## Slide 4: How to represent vehicle specific instantiations in VSS-core
Pass car instance config:
"Axle": [
"Row[1,2]",
[
["Left","Right"],
["Left","Right"]
]
]
Truck instance config:
"Axle": [
"Row[1,3]",
[
["Pos6","Pos10"],
["Pos6","Pos7", "Pos9","Pos10"],
["Pos6","Pos7", "Pos9","Pos10"]
]
]
Himconfiguration.json declaration

## Slide 5: How to represent vehicle specific instantiations in VSS-core
Chassis.Axle:
instances0: 0 #Axle
type: branch
description: Axle signals
#include Axle.vspec2 Chassis.Axle
....
Wheel:
instances1: 0 #Axle
type: branch
description: Wheel signals for axle
#include Wheel.vspec Wheel
VSS-core vspec2 declaration:

## Slide 6: VSS-core conclusions
A few larger branches can be removed
Further pruning is possible, but is more on per signal level.
Vehicle type specific instantions can be represented in VSS-core.
  If app developers accept minor adaptations per vehicle type.
The HIMconfiguration.json file contains all that is needed to deploy a vehicle specific type and model.

## Slide 7: VSS supplementary data
Vehicle.Body.*:
Vehicle.Body.Hood
Vehicle.Body.Horn
Vehicle.Body.Lights
Vehicle.Body.Mirrors
Vehicle.Body.Trunk
Vehicle.Body.Windshield
Vehicle.Cabin.*:
Vehicle.Cabin.Door
Vehicle.Cabin.HVAC
Vehicle.Cabin.Infotainment
Vehicle.Cabin.Light
Vehicle.Cabin.RearShade
Vehicle.Cabin.RearviewMirror
Vehicle.Cabin.Seat
Vehicle.Cabin.Sunroof

## Slide 8: VSS supplementary data
Vehicle.Chassis.*:
Vehicle.Chassis.Axle
Vehicle.Chassis.Brake
Vehicle.Chassis.ParkingBrake
Vehicle.Chassis.SteeringWheel
Vehicle.MotionManagement.*:
Vehicle.MotionManagement.Brake
Vehicle.MotionManagement.ElectricAxle
Vehicle.MotionManagement.Steering
Vehicle.Powertrain.*:
Vehicle.Powertrain.CombustionEngine
Vehicle.Powertrain.ElectricMotor
Vehicle.Powertrain.FuelSystem
Vehicle.Powertrain.TractionBattery
Vehicle.Powertrain.Transmission
Vehicle.Occupant.*:
Vehicle.Occupant.RowX