## Slide 1: Aos for In-Vehicle Edge Computing
Cloud-and-vehicle framework as an example
of CVII-related ongoing development

## Slide 2: Data lake in the Cloud (or Telco Edge)
VSS data representation
Enterprise data
representation
VSS data representation
Backend services
transformation
processing
Amount of data? Streaming / bulk data vs. network traffic limitations
Offline reactions not possible
Only standardized by OEM data representation
Data flow
Vehicle
Cloud

## Slide 3: Edge computing on vehicles
VSS data representation
Enterprise data
representation
Edge service
Backend services
Container
Data flow
Control flow
Data flow can be reduced
Any representation possible, internal to enterprise logic or standardized (e.g. ExVe, …)
Offline reactions

## Slide 4: Aos platform
Microservices orchestration on embedded systems
End-to-end secured OTA management
Modern software development approach for constrained environments
Multi-access edge computing for vehicles
Monitoring & Control
Microservices deployment
Service Data
Operation
OEM Aos Cloud
OEM
Microservice
deployment
Service Provider Cloud
Service Provider
Operation
Delivery
OCI-Compliant Containers
AMQP Command & Control
Campaign Planning
Scaling
Security
System Isolation
Containers
Cloud Connection
Service Runtime Introspection
Multi-tenancy
Control Roles
Usage Roles
Device Level Service Isolation
Local Storage Support
Device Data
Inter-service communication
Protected Hardware access
Data abstraction model (VISS)
HW Provisioning Template
Development SDK
Modern SW Frameworks
Service Debugging Tools
Runtime Platform Alerts
Service Validation Tools
ECU/TCU
OTA

## Slide 5: OCI specifications
Gaps
  Device access
  Automated service discovery
  Not enough quota configs
  API access rights
Specifications
  Image manifest
  Image specification
  Runtime specification
De-facto industry standard: used by Docker, Podman, OpenShift, …

## Slide 6: Aos Service YAML description
  Aos Service YAML → OCI Image Manifest + OCI Image Config + Aos Service Config → OCI Runtime Spec
  Aos Service YAML is a human-readable configuration
  Service config covers OCI gaps
    Extended quotas such as network, storage and state
    Extended security configuration such as no-update TTL, allowed inbound connections
    DNS configuration for automatic service discovery
    Devices, mounts and system resources directly accessible from container
    API permissions → VISS used
  Implementation and spec being published, Apache 2.0 license

## Slide 7: In-vehicle data access with Aos
  Each Service has its own certificate to authorize itself
  Services’ API permissions are populated to VIS Server which provide data access to an authorized services accordingly
    Transport must support mTLS, e.g. websockets
  All of the in-vehicle data represented by VSS
    … extensions are possible e.g. ExVe or ViWi or anything custom, but better stick to VSS
  Each edge service may perform any non-standard transformation or processing of standardized vehicle data into whatever the rest of its backend expects
  Or send some or all vehicle data to a data lake in the cloud when it needs to (events based)

## Slide 8: Distributed identification & authorization with global IDs
OEM B
OEM A
  User identification & service configuration mapping
    Vehicle users shall be uniquely identified across different OEMs
    Common authorization mechanism – which user can access which vehicle
  Service identification
    Services from different OEMs shall be uniquely identified to allow inter-vehicle user settings migration
    Standardized approach to discovery & communication using service catalogs / DNS
Vehicle 1
Vehicle 2
SID: 21216
SID: 43437
SID: 98731
UID: 12345
Auth type 1
Auth type 2
UID: 12345 ?
UID: 12345 – service stack
UID: 12345
Map Auth to UID

## Slide 9: THANK YOU