## Slide 1: Workshop
Automotive Push Notification Protocol
29.01.2024

## Slide 2: Problem Statement
“A push notification (also known as a server push notification) is the delivery of information to a computing device from an application server where the request for the transaction is initiated by the server rather than by an explicit request from the client“ [1]
Common use-cases:
  Delivery of messages
  Incoming VoIP calls
  Live updates in a running app (e.g., update list of upcoming meetings)
Problem:
  Apps get killed by the system and cannot rely on being able to communicate with their backend
  There exists no standardized push notification service for AOSP

## Slide 3: Goal of This Workshop
Align on a common AOSP push notification service
  Reduce fragmentation as much as possible
  Agree on a common ground to ensure compatibility across OEMs
  Allow 3rd parties to build once and deploy anywhere (outside of GAS)
Define the minimum common ground for the minimum set of functionality for such a push notification service
Focus will be on the 1-1 communication channel from 3rd party application servers to a specific app instance (not to any specific app)
Focus is on Android Automotive Apps working independently of a customers brought in device (not phone projection)
Its not about the notifications, its about pushing a message to the car

## Slide 4: Topics For This Workshop
Discuss the proposal
  does this work for everyone?
Need to specificy more than Web Push (RFC8030) does?
  Like message delays, rate limits etc.
Discuss integration and hosting strategy for OEMs
Discuss reference implementation
Discuss testing suite
Discuss working model with UnifiedPush

## Slide 5: What is out there
  Apple Push Notification service (APNs) – only usable on Apple devices
    https://developer.apple.com/documentation/usernotifications
  Firebase Cloud Messaging (FCM) – only usable with Google’s Play services / Google Automotive Services
    https://firebase.google.com/docs/reference/fcm/rest/v1/projects.messages?hl=en#AndroidConfig
  Huawei Mobile Services (HMS) – only usable on Huawei devices
    https://developer.huawei.com/consumer/en/doc/HMSCore-References/https-send-api-0000001050986197#EN-US_TOPIC_0000001562768322__p153162820230
  Amazon Device Messaging (ADM) – only usable on Amazon devices
    https://developer.amazon.com/docs/adm/overview.html
  Web Push (RFC8030) – THE standard for browsers
    https://developer.mozilla.org/en-US/docs/Web/API/Push_API
  UnifiedPush – a Web Push inspired protocol for native applications on Android and Linux
    https://unifiedpush.org/

## Slide 6: Beware
Firebase Cloud Messaging is both:
  the official push service for Chrome and Android
  a commercial push service that can send notifications to APNs, Web Push and Android, similar to Pushpad, OneSignal, Pushy and others.
Regardless of what we do, our solution will not be compatible with Firebase (unless Google adds us as a platform)
See: https://firebase.google.com/docs/cloud-messaging/fcm-architecture
We want to standardize for the automotive space

## Slide 7: Similarities
A push notification service generally consists of four parts
Notifications are triggered by an HTTP POST request to the respective service
The exact type of the connection between the distributor and the push server varies
  This part has a big influence on the energy efficiency and each vendor has its own secret sauce
The mechanism used by the distributor to talk to the application depends on the platform
  On Android this is done using Intents
Push Server
Distributor
App
3rd Party
Application Server
3rd Party
Application
HTTP based interface
Platform specific IPC (e.g., Intents)

## Slide 8: Proposal

## Slide 9: Proposal
From previous analysis performed independently by different parties – Faurecia Aptoide, BMW, FORVIA - UnifiedPush seemed the most promising solution:
  Provides a specification
  OEMs have freedom to select their solution (implement their own or use an existing one compatible with the spec)
  Apache 2.0 licensed, same as AOSP
  Compatible with Web Push (transition for 3PAs simpler since some of them already support it)
However, it does not support any of the industry standard features like:
  Application Server Authentication
  Time-to-live
  Urgency
  Push message receipts
  Replacing/Updating Push Messages

## Slide 10: Proposal
Integrated /Provided by the OEM
Provided by the 3rd party
Push server
corresponding to the distributor app
Distributor
App
3rd Party
Automotive
App
3rd Party
Application Server
Adapt and extend the existing UnifiedPush specification1
1 Changes to the UnifiedPush Android specification are necessary to support all features from RFC8030 and RFC8292.
(RFC8030
+RFC8291
+RFC8292)
Web Push
Extend UnifiedPush to support these features
  Push server <-> app server API: switch to a fully Web Push compatible API
  Client side <-> App-Distributor API: extend the existing UnifiedPush specification to support the changes in the server side API
Keeps the main characteristics of UnifiedPush
  All distributors are compatible with all apps
  Separate specification for the server and the client giving a lot of freedom to the implementation

## Slide 11: Proposal – Necessary Changes to UnifiedPush
Integrated / Provided by the OEM
Provided by the 3rd party
Push server
corresponding to the distributor app
Distributor
App
3rd Party
Automotive
App
3rd Party
Application Server
Adapt and extend the existing UnifiedPush specification1
1 Changes to the UnifiedPush specification are necessary to support all features from RFC8030 and RFC8292.
(RFC8030
+RFC8291
+RFC8292)
Web Push
Server side: full rewrite of the specification
  Existing services that support UnifiedPush (i.e., ntfy.sh) won’t be compatible with the new spec
Client side: only minor changes needed
  Make the existing MESSAGE_ACK feature mandatory
  Add the mandatory option to include a VAPID key in the REGISTER intent

## Slide 12: VAPID: Voluntary Application Server Identification
VAPID answers the following questions:
Who sends the notification?
Are they allowed to send notifications to the car?
OEM
Push Server
3rd Party
Application Server
OEM custom interface
3rd party custom interface
Create a Public/Private key pair
Include the public key in the app and include it when subscribing to push notifications
Create a new URL endpoint that only accepts requests signed with the private key associated with the provided public key
Include a signed JWT containing some contact information in every push notification request
OEM
Distributor
App
3rd Party
Automotive
App
How VAPID works:

## Slide 13
Push Server
3PA App Server
Distributor
org.unifiedpush.android.distributor.REGISTER
org.unifiedpush.android.distributor.UNREGISTER
org.unifiedpush.android.distributor.MESSAGE_ACK
3PA
org.unifiedpush.android.connector.NEW_ENDPOINT
org.unifiedpush.android.connector.MESSAGE
org.unifiedpush.android.connector.UNREGISTERED
org.unifiedpush.android.connector.REGISTRATION_FAILED
NEW_ENDPOINT (Token, Endpoint) or REGISTRATION_FAILED
REGISTER (Application, Token, VAPID key)
SetPushSubscription (Endpoint, <3PA specific client id>))
Interactions between Distributor and Push server are not defined by Unified Push
PushMessage: Post (Message, signed VAPID JWT, TTL, Urgency, etc.)
Unique endpoint associated with the token: RFC 3987
ENDPOINT Get
{"unifiedpush":{"version":1}}
Result (2xx OK, 4xx error)
web push protocol RFC8030
PushMessage: Post (Message)
Registration / Subscription
Distribute Subscription
UnifiedPush specific (?)
MESSAGE (Token, Message, ID(optional))
MESSAGE_ACK (ID)
Send Push Message
CancelPushSubscription (Endpoint, <3PA specific client id>))
UNREGISTER (Application, Token)
UNREGISTERED
Proposal - Sequence Diagrams
Notes: https://www.w3.org/TR/push-api/
https://unifiedpush.org/spec/android/
https://unifiedpush.org/spec/server/

## Slide 14: Proposal – OEMs
Integrated / Provided by the OEM
Provided by the 3rd party
Push server
corresponding to the distributor app
Distributor
App
3rd Party
Automotive
App
3rd Party
Application Server
Adapt and extend the existing UnifiedPush specification1
1 Changes to the UnifiedPush specification are necessary to support all features from RFC8030 and RFC8292.
(RFC8030
+RFC8291
+RFC8292)
Web Push
OEMs:
  Integrate a distributor app on the Head Unit
    Custom implementation
    Other 3rd party implementation
  The chosen distributor app is linked to a push server meaning that depending on the chosen distributor your cars will use either
    Your own infrastructure
    The infrastructure of you distributor supplier
Compatibility between all the different implementations will be ensured by a COVESA developed testing suite

## Slide 15: Proposal – 3rd Parties
Integrated / Provided by the OEM
Provided by the 3rd party
Push server
corresponding to the distributor app
Distributor
App
3rd Party
Automotive
App
3rd Party
Application Server
Adapt and extend the existing UnifiedPush specification1
1 Changes to the UnifiedPush specification are necessary to support all features from RFC8030 and RFC8292.
(RFC8030
+RFC8291
+RFC8292)
Web Push
3rd Parties:
  Client side: Integrate their app with the provided connector library (slightly changed from the existing UnifiedPush one)
  Backend side: Integrate Web Push functionality if not already existing

## Slide 16: Outlook
Extend this 1-1 message channel to a more fully fledged push service

## Slide 17: Thank you!

## Slide 18: Backup

## Slide 19: Time to live (TTL)
How long the message should be kept in the push server storage if the device is offline. Some push messages are not useful once a certain period of time elapses.
Example:
Short TTL: Imcoming call
Long TTL: New content in a social media app

## Slide 20: Urgency/Priority
To avoid consuming resources to receive trivial messages, it is helpful if an application server can communicate the urgency of a message and if the user agent can request that the push server only forwards messages of a specific urgency.
Example:
Low urgency: Advertisement
High urgency: Incoming call

## Slide 21: Push message receipts
A way for application servers to know when a given notification was actually delivered to a device/app.

## Slide 22: Encryption
Encrypt the content of push messages.

## Slide 23: Replace push messages
A push message that has been stored by the push service can be replaced with new content. If the user agent is offline during the time that the push messages are sent, updating a push message avoids the situation where outdated or redundant messages are sent to the user agent.
Example:
Updating the score of a soccer match