## Slide 1: Vehicle Information Service Specification Status Update
AMM Sept 2024

## Slide 2: VISS quick history
“FAT” API for browser runtime @W3C - 2014
JLR proposed Remote Vehicle Interface (RVI) @GENIVI introducing VSS - 2016
Critique of API by W3C Device and Sensors group
Vehicle Information Service Specification (VISS) started - 2016, v1 2016
  Splits API from Dara model (VSS)
  WebSocket and JSON, no Authentication, Access Control, etc
  VISSv1 known implementation by Melco, Volvo and JLR (Visteon), Bosch Kuksa.val
Volkswagon ViWi makes a Member Submission to W3C - 2016
VISSv2
  Reference implementation, BMW, Bosch, other?
  W3C Automotive Working Group closes and transfers VISS to COVESA - 2023
  Finalize version 2 release - 2024
  Adoption by AutoSAR - 2023
VISSv3 - subject of this presentation

## Slide 3: VISS overview
A few of the basic features
Separate API from data model (VSS)
  Experimentation to support additional data models (Hierarchical Information Model - HIM)
Get/set/subscribe methods
Supports multiple protocols - WebSocket, HTTPS, MQTT, gRPC
Includes Access Control, Authentication, hooks for consent management

## Slide 4: VISS project overview
The first COVESA VISS release was published just before spring AMM: version 2.0
  https://github.com/COVESA/vehicle-information-service-specification/releases/tag/v2.0
The development of the next version 3.0 was started after the spring AMM.
New features:
  Message payload is the normative definition, transport protocol selection is non-normative.
  Message payload primary format is JSON, but it may be encoded during client-server transition. This shall be documented in the Payload Encoding specification (Protobuf).
  Different transport protocols may introduce minor deviations, but this must then be documented in the Transport Protocol Examples specification (GPRC).
  Upload/Download file transfer is under discussion to be supported over selected transport protocols.
  A more fine-grained server capabilities solution is under development.
  Extended error code set (502 bad_gateway, 504 gateway_timeout, 408 request_timeout, 429 too_many_requests)

## Slide 5: AUTOSAR Automotive API
AUTOSAR has decided to use VSS and VISSv2.0 for the Automotive API.
From the Automotive API Explainer document:
  The objective of the Automotive API is to establish a standardized access to read and write vehicle data from both on-board and vehicle external applications (e.g., a cloud server), while simultaneously letting the data and services have their project-, OEM-specific definitions and representations in the in-vehicle network.
  To facilitate access to the Automotive API a network interface, a communication protocol is required. The interface is to use the VSS vehicle data model. For that purpose, the Vehicle Information Service Specification version 2 (VISS) was chosen.
  Crucially, the new interface is intended to be useable by individuals and organizations that are not members of AUTOSAR. This approach will contribute to the connected vehicle ecosystem, driving innovation, further development and compatibility across all vehicles and applications using the new interface.

## Slide 6: VISSR project overview
The experimental gRPC support was thoroughly tested in a spring AMM demo.
  Empowering Digital Services-PDF
  Empowering Digital Services - Demo
The VISSR gRPC proto file was used in the coming VISSv3.0 Payload Encoding specification for defining the gRPC encoding.
The VISSv2.0 consent model support was thoroughly tested in a spring AMM demo.
  VISS Consent Model Explained and Demoed – PDF
  VISS Consent Model Explained and Demoed - Demo
The plan is to implement the new features in the coming VISSv3.0 specification. This will require a branching structure that separates version 2.0 from 3.0.
A refactoring of the current usage of server polling of the state storage is in the planning, replacing it with an event-based model.

## Slide 7: Get involved
Join VISS Expert Group
Try it out in the COVESA Playground