## Slide 1
Hands-On
May 10, 2017 | ALSA Routing Adapter Plugin
Jens Lorenz
Staff Engineer, ADIT GmbH, GENIVI Alliance

## Slide 2: Why ALSA Routing Adapter?

## Slide 3: Overview
Existing Infrastructure
  Daemon
  Plugins
    CommonAPI
    DBus
    Generic Controller

## Slide 4: Motivation
Reduce learning curve
  Playground to understand domain concept
  Playground to understand static vs. dynamic IDs
Playground independent of audio server
  AM works as a single daemon
  ALSA plugins for processing only i.e. mixing
Works with Generic Controller
Usable for real products
  Used in platforms with Hands-Free (ECNR) systems

## Slide 5: What does it?

## Slide 6: Design
Domain Database
  Filled on construction
  Registered on startup
Streaming Control
  Creates Proxies on demand
  Proxies can be replaced
Volume Control
  Works with SoftVol
ALSA Control
  On SoundProperty Request

## Slide 7: Proxy in Audio

## Slide 8: Proxy Interface
class IAmRoutingAdapterALSAProxy
{
  IAmRoutingAdapterALSAProxy(const ra_Proxy_s & proxy);
  virtual ~IAmRoutingAdapterALSAProxy();
  virtual am_timeSync_t getDelay() const = 0;
  virtual am_Error_e openStreaming() = 0;
  virtual am_Error_e startStreaming() = 0;
  virtual am_Error_e stopStreaming() = 0;
  virtual am_Error_e closeStreaming() = 0;
}

## Slide 9: Example Needed?

## Slide 10: Domain Configuration with Gateway
<amra_alsa>
<tDOMAIN domNam = "Applications" nodNam = "Cpu">
<tSOURCE srcNam = "MediaPlayer" srcID = "1" srcClsNam = "BASE" />
<tSINK sinkNam = "GatewayIn" visible = "0“ />
</tDOMAIN>
<tDOMAIN domNam = "VirtDSP" nodNam = "Cpu">
<tSOURCE srcNam = "GatewayOut" srcClsNam = "BASE" visible = "0">
<tGATEWAY gatewayNam = "Gateway" sinkNam = "GatewayIn" sinkDomNam = “Applications"
lstSrcFrmt = "2" lstSinkFrmt = "2" convertionMatrix = "1"> </tGATEWAY>
</tSOURCE>
<tSINK sinkNam = "AMP" sinkID = "1“ />
</tDOMAIN>
</amra_alsa>

## Slide 11: Volume Configuration
<tDOMAIN domNam = "Applications" nodNam = "Cpu">
<tSOURCE srcNam = "MediaPlayer" srcClsNam = "BASE"
pcmNam = "vdev_app_mediaplayer" volNam = "vol_mediaplayer" />
<tSINK sinkNam = "Gateway" visible = "0" />
</tDOMAIN>
ALSA configuration:
pcm.vdev_app_mediaplayer {
type plug
slave.pcm vdev_mpsv
}
pcm.vdev_mpsv {
type softvol
slave.pcm “hw:Loopback,0"
control.name vol_mediaplayer
control.card 0
}

## Slide 12: Proxy Configuration
<tDOMAIN domNam = "VirtDSP" nodNam = "Cpu">
<tSOURCE srcNam = "Gateway" srcClsNam = "BASE" visible = "0“ />
<tSINK sinkNam = "AMP" sinkID = "1“ />
<tPROXY srcNam = "Gateway" sinkNam = "AMP“
pcmSrc = "vdev_dsp_gateway“ pcmSink = "vdev_dsp_amp“
lstRates = "48000" msBuffersize = "8"
CPUSchedulingPolicy = "1" CPUSchedulingPriority = "80" />
</tDOMAIN>
ALSA configuration:
pcm.vdev_dsp_gateway {
type hw
slave.card “Loopback”
slave.device 0
}
pcm.vdev_dsp_amp {
type dmix
slave.pcm “hw:0”
slave.rate 48000
slave.channels 2
}

## Slide 13: Sound Properties
<tDOMAIN domNam = "VirtDSP" nodNam = "Cpu">
<tSOURCE srcNam = "Gateway" srcClsNam = "BASE" pcmNam = "vdev_app_mediaplayer" />
<tPROPERTY type = "1">
<tPROPSPEC value = "1"
namsVals = "vol_mediaplayer, 50; ADC High-Pass Filter, High Pass;" />
<tPROPSPEC value = "2"
namsVals = "vol_mediaplayer, 200; ADC High-Pass Filter, None;" />
</tPROPERTY>
</tSOURCE>
</tDOMAIN>

## Slide 14: Next?

## Slide 15: Open Topics
Generic Controller works with fix topology
  Policy shall work even without fixed configured topology
USB sound card detection support
  Sound cards will be registered to AudioManager / HMI
  Proxy can be used to integrate new detected devices

## Slide 16
genivi-audio-manager@lists.genivi.org
jlorenz@de.adit-jv.com
References
https://github.com/GENIVI/AudioManager
https://github.com/GENIVI/AudioManagerPlugins
Questions?

## Slide 17
Visit GENIVI at http://www.genivi.org or http://projects.genivi.org
Contact us: help@genivi.org
This work is licensed under a Creative Commons Attribution-Share Alike 4.0 (CC BY-SA 4.0) GENIVI is a registered trademark of the GENIVI Alliance in the USA and other countries. Copyright © GENIVI Alliance 2017.
Thank You!